## Slide 1: CS3744 GUI Programming & Graphics
© 2010 Roger Ehrich
Department of Computer Science
28 - Intro to Graphics: Color
Notes: Virginia Tech Masters of Information Technology graduate program.
CS 5044, Object-oriented programming with Java.
Course introduction.

## Slide 2: The Eye
Department of Computer Science
CS 3744: Color
108 rods, sensitive, color
insensitive.
6106 cones, mostly in fovea.
Fovea is 1.5 mm in diameter,
150,000 cones / mm2 or 337,000
elements.
Color vision adaptive over
intensity range of 106.
Overall adaptivity of 1010.
<number>

## Slide 3: Receptor Distribution
Department of Computer Science
CS 3744: Color
<number>

## Slide 4: Visible Spectrum
Department of Computer Science
CS 3744: Color
<number>

## Slide 5: Spectral Sensitivity
Department of Computer Science
CS 3744: Color
<number>

## Slide 6: Light Sensation
Department of Computer Science
CS 3744: Color
Color depends on:
Object surface physics
Spectral composition of light sources
Geometry of the world model
Human visual system
Achromatic light
Intensity, luminance (physical measures)
Brightness (psychological measure)
<number>

## Slide 7: Intensity Scale
Department of Computer Science
CS 3744: Color
Suppose we want to display 256 intensities. How should they be selected? Eye is sensitive to ratios, not to absolute values.
Let I0 be the minimum intensity, 1.0 the maximum. Each intensity is r times as bright as its predecessor, ie,
I0, I0r, I0r2, I0r3, I0r4, …, I0r255 = 1
So for n+1 intensities, r = (1/I0)1/n.
For a CRT, I0 = .005 to .025; 1/I0 is the dynamic range.
<number>

## Slide 8: Intensity Scale (cont.)
Department of Computer Science
CS 3744: Color
How do we get display devices to display a correct intensity scale, given the device nonlinearities? Gamma correction.
How many intensity levels are enough to establish a visually continuous intensity scale? r < 1.01. Then
n = log1.01 (1/I0)
Typical dynamic ranges:
CRT and Photographic prints ~100 n ~ 500
Slide transparencies ~1000 n ~ 700
B&W newsprint ~10 n ~ 250
<number>

## Slide 9: Psychology of Color
Department of Computer Science
CS 3744: Color
Basic terminology:
Hue: Basic distinguishing feature of color
Saturation: How much white is added to the color
Lightness: How much intensity is perceived
Artist terminology (preserves hue):
Tint: How much white pigment is added
Shade: How much black pigment is added
Tone: The over all color effect
<number>

## Slide 10: Colorimetry
Department of Computer Science
CS 3744: Color
Need an objective way of specifying colors!
Perceptual Term Colorimetric Term
Hue Dominant wavelength
Saturation Excitation purity
Lightness (reflecting objects) Luminance
Brightness (self luminous) Luminance
<number>

## Slide 11: Tristimulus Theory
Department of Computer Science
CS 3744: Color
Many color display devices are modeled after the human eye which has three different types of color receptors.
Consider color reproduction devices that have three different color stimulants, called R=red, G=green, and B=blue. Then
a particular color is obtained by color addition as
T = aR + bG + cB
and for color matching purposes, normalize brightness by requiring that a + b + c = 1.
<number>

## Slide 12: Color Matching
Department of Computer Science
CS 3744: Color
Illuminate half a disk with a test color and then determine a mixture of 3 primaries to provide a match on the other side of the disk.
Colors can be realized only within the tristimulus triangle. Colors with negative coefficients are unrealizable.
If T is not achievable with the primaries provided, then it must be desaturated by adding a primary on the left side of the equation. The resulting chromaticity diagrams may be quite different if different primaries are used.
<number>

## Slide 13: Color Matching (cont.)
Department of Computer Science
CS 3744: Color
Wright (1928): R=650, G=530, B=460 Guild (1931): R=700, G=547, B=436
<number>

## Slide 14: Color Matching (cont.)
Department of Computer Science
CS 3744: Color
Typical color matching functions:
Red = 700, Green = 546.1, Blue = 435.8
<number>

## Slide 15: CIE (1931)
Department of Computer Science
CS 3744: Color
Standard observer matching functions:
Let
X =  E() x() d
Y =  E() y() d
Z =  E() z() d
Then let
x = X / (X + Y + Z)
y = Y / (X + Y + Z)
z = Z / (X + Y + Z)
So that x + y + z = 1
<number>

## Slide 16: CIE Chromaticity Diagram
Department of Computer Science
CS 3744: Color
<number>

## Slide 17: CIE Color Sensitivity
Department of Computer Science
CS 3744: Color
Statistical variation of
chromaticity matches
in different parts of
the CIE diagram
(Judd and Wyszecki)
<number>

## Slide 18: MacAdam’s CIE Transformation (1937)
Department of Computer Science
CS 3744: Color
<number>

## Slide 19: Properties of the CIE Diagram
Department of Computer Science
CS 3744: Color
Saturated colors are on the boundary.
Standard illuminant D65 (daylight) is 6504K.
Luminance is factored out of the CIE diagram.
Parallel planes where x+y+z  1 represent other luminances.
Complementary colors are those that can be mixed to produce white light.
To determine dominant wavelength of a color c, draw a line from the white point through c and determine where it intersects the boundary.
<number>

## Slide 20: Color Gamut
Department of Computer Science
CS 3744: Color
Reproduction devices cannot display all colors, but many cameras allow selection of standard gamuts. No gamuts are in effect in RAW mode.
sRGB Adobe RGB
<number>

## Slide 21: XYZ from RGB
Department of Computer Science
CS 3744: Color
The CIE coordinates can be determined from RGB space by a linear transformation
X = R XR + G XG + B XB
Y = R YR + G YG + B YB
Z = R ZR + G ZG + B ZB
where the 9 transformation components are functions of the XYZ tristimulus values, the XYZ white point coordinates, and the luminance of the white point.
<number>

## Slide 22: Printers and CMYK
Department of Computer Science
CS 3744: Color
Displays use additive colors while printers use subtractive colors.
Additive (RGB) Subtractive (CMY)
<number>

## Slide 23: Printers and CMYK (cont.)
Department of Computer Science
CS 3744: Color
Printers usually use black ink in addition to CMY because:
Text is usually printed in black and it is important to maintain color purity on edges and fine detail.
A combination of 100% CMY inks soaks the paper and causes spreading.
A combination of 100% CMY often results in a muddy brown.
Black ink is less expensive than using multiple inks.
K = min (C, M, Y)
C = C - K where C = 1 - R
M = M - K where M = 1 - G
Y = Y - K where Y = 1 - B
<number>

## Slide 24: RGB Color Model
Department of Computer Science
CS 3744: Color
Convenient for display devices:
<number>

## Slide 25: YIQ (NTSC) Color Model
Department of Computer Science
CS 3744: Color
Convenient for commercial broadcasting – note that the Y component is luminance and is heavily weighted toward green.
Y = .299 R + .587 G + .114 B
I = .596 R - .274 G - .321 B
Q = .211 R - .523 G + .311 B
<number>

## Slide 26: YUV (PAL and Secam) Color Model
Department of Computer Science
CS 3744: Color
Convenient for international broadcasting – note that the Y component is luminance and is heavily weighted toward green as in the YIQ model.
Y = .299 R + .587 G + .114 B
U = -.147 R - .289 G + .436 B
V = .615 R - .515 G - .100 B
<number>

## Slide 27: HSV=HSB Color Model
Department of Computer Science
CS 3744: Color
Corresponds to a projection down the diagonal of the RGB color cube (including Photoshop).
<number>

## Slide 28: HLS Color Model
Department of Computer Science
CS 3744: Color
Includes Paintshop Pro. HSI (Tektronix) is similar, except that the formulas are slightly different. S=1 if any component is 0 and S=0 if R=G=B.
<number>

## Slide 29: YPbPr (analog) and YCbCr (digital) Color Models
Department of Computer Science
CS 3744: Color
The Y component is identical to YUV and YIQ. The digital components are obtained by scaling and offset from the analog values.
<number>
Y = .299 R + .587 G + .114 B
Pb = -.168 R - .331 G + .500 B
Pr = .500 R - .419 G - .081 B

## Slide 30: L*a*b* (CIELAB) Color Model
Department of Computer Science
CS 3744: Color
L is lightness with values 0 to 100 and a and b are color dimensions. This is based on the 1931 CIE XYZ space but more representative of the logarithmic way humans see color.
L* = 116 f (Y/Yn) – 16
a* = 500 [ f (X/Xn) – f (Y/Yn) ]
b* = 200 [ f (Y/Yn) – f (Z/Zn) ]
where
f(t) = t1/3 for t > .008856
f(t) = 7.787 t + 16/116 otherwise
and
Xn, Yn, Zn are the XYZ CIE coordinates of the white point.
<number>

## Slide 31: Digital Image Sensors
Department of Computer Science
CS 3744: Color
Note that except for Foveon sensors and 3-chip cameras, digital camera sensors are monochromatic, and color must be interpolated from sparse measurements.
<number>

## Slide 32: RAW Digital Camera Formats
Department of Computer Science
CS 3744: Color
RAW mode imaging has great advantages over JPEG!
Quality cameras have 12-bit or 14-bit photosites, whereas JPEG is limited to 8-bits per color.
Color temperature, color space, contrast, and exposure can be determined after the files have been downloaded from the camera.
Many of the best demosaicing algorithms are too computationally intensive to run in real time on the camera itself.
<number>